## Slide 1: Smart Glove for Fist Dance
Shiyi Tang, Yan Zhu, Bohan Diao

## Slide 2: Introduction: Fist Dance
Shake hands for first four beats​
Any actions for next four beats​
  Rock paper scissor for next two beats​
  Point to a direction for next two beats​
If "win rock paper scissor" & "both point to the same direction" :​
  Victory!!!​
Else​
  Repeat

## Slide 3: Introduction: basic idea
Game participant: 1 person, 1 computer
The person will wear a custom built data glove with flex sensors and IMU​
The ML model will make a prediction about the person’s gestures.​
The computer will play with the person according to the prediction of the ML model. ​

## Slide 4: Hardware
Arduino Due
5 Flex Sensors: On each finger Soldered onto wires to measure finger bending.
1 IMU: On the back of the glove Stick to the glove to capture motion and orientation of the hand.
Polyester Knit Glove with Kapton tape

## Slide 5: Hardware
Flex
  Sticked on the glove
  Connected to the Arduino Due using a voltage divider circuit
IMU
  Attached to the back of the glove with pull-up resistors

## Slide 6: Data collection
7 gestures (Rock, Paper, Scissors and 4 directions)
Rock Paper Scissor
Up Down Left Right

## Slide 7: Data collection
Playing sequence in each trial:
  Rock, Up, Paper, Up, Scissors, Up, Rock, Down, Paper, Down, Scissors, Down, Rock, Left, Paper, Left, Scissors, Left, Rock, Right, Paper, Right, Scissors, Right, Rock
  24 transitions
80 Trials collected
Sampling rate: 50 HZ

## Slide 8: Data labelling
Automatic
Use acceleration data to determine the beats

## Slide 9: Data labelling

## Slide 10: Data labelling
24 transitions
2 beats for each gesture
(24+1) * 2 = 50 beats
✊
✊
⬆️
⬆️
⬆️
⬆️
⬆️
⬆️
✌
✌
🖐️
🖐️

## Slide 11: Data labelling
24 classes: 24 transitions

## Slide 12: Data labelling
Window size = 15
Step size = 1
Data dimension: (n, 15, 11)
Data pre-processing
IMU data:
  Moving average
  Window size = 5
Flex data:
  Median filtering
  Kernal size = 3
Normalization

## Slide 13: Training
Model: LSTMClassifier(input_size=11, hidden_size=64, num_layers=3, num_classes=24, dropout=0.3)

## Slide 14: Training
Model
  LSTM: input size 11, hiddden_size 64, num_layer 3, num_class 24
optimizer
  Adam: learning rate 2e-3, weight decay 1e-5
loss function
  CrossEntropyLoss
Training hyperparameter
  batch size 32, 100 epoch with early stopping, patience 10
Training hardware
  single A100 from colab

## Slide 15: Training pipeline
Stage A
  pretrained on massive recorded(80000+) data from more diversed sources
stage B
  finetuning on relatve smaller(6000+) dataset from single source
stage C
  finetuning on small dataset recorded on new hardware,due to some hardware failures.

## Slide 16: Training & Validation
Training:

## Slide 17: Offline Performance
Model performance
  Training data
    Training data A, hardware A(pretraining):
      80% from Yan Zhu and Diao Bohan
      20% from various classmates
      80000 samples in 200hz, downsampled to 20000 samples in 50hz
      Acc ~62%
    Training data B, hardware A:
      6000 samples in 50hz from Yan Zhu
      Acc ~ 81%
    Training data C, hardware B(new flex sensors for two fingers due to hardware failures):
      3000 samples inn 50hz from Yan Zhu
      Acc ~ 93%, Precision 95%+
  Test data
    Test data : Yan Zhu (some unseen data recorded with hardware B)

## Slide 18: Offline Performance
Gesture | Up | Down | Left | Right
Rock | 0.9932 | 0.9952 | 0.0000 | 0.5714
Paper | 0.3333 | 0.1250 | 0.7500 | 0.9832
Scissor | 0.5000 | 0.5714 | 0.3000 | 0.6250
Up | 0.6364 (→Rock) | 0.9943 (→Paper) | 0.5238 (→Scissor) | 
Down | 0.9983 (→Rock) | 0.6667 (→Paper) | 0.3846 (→Scissor) | 
Left | 0.9978 (→Rock) | 0.7500 (→Paper) | 0.4286 (→Scissor) | 
Right Overall Prc 81%+ | 0.3333 (→Rock) | 0.9854 (→Paper) | 0.4286 (→Scissor) | 

## Slide 19: Offline Performance
Bad case analysis:
Problem: Performance of left-related gestures is lower compared to other directions
Analysis: Left gestures confused with other directions (same hand gesture as UP but different orientation).
Solution: Increase High-Quality Left Gesture Data

## Slide 20: Real time prediction
Beat detection and Gesture prediction run in parallel threads
Beat detection:
  Store new data in a sliding window (300 ms)
  Find accel_values peak
    Put the newest window data to prediction_queue
  To avoid double-triggering of beats, set up a BEAT_COOLDOWN
Gesture prediction:
  Get the data from prediction_queue

## Slide 21: Real time prediction
Also tried a voting mechanism
Use several windows before the beat and choose the most common prediction
Useful when the model is not accurate enough

## Slide 22: Offline Performance Final
Gesture | Up | Down | Left | Right
Rock | 0.8750 | 0.9678 | 0.9875 | 0.9894
Paper | 0.9932 | 0.9924 | 0.9985 | 0.9942
Scissor | 0.9954 | 0.9986 | 0.7500 | 0.6667
Up | 0.8871 (→Rock) | 0.8950 (→Paper) | 0.9965 (→Scissor) | 
Down | 0.9934 (→Rock) | 0.9367 (→Paper) | 0.9954 (→Scissor) | 
Left | 0.8333 (→Rock) | 0.9915 (→Paper) | 0.9986 (→Scissor) | 
Right Overall Prc 93%+ | 0.9954 (→Rock) | 0.9875 (→Paper) | 0.8182 (→Scissor) | 

## Slide 23: Real time prediction
Designed an user interface
Display gestures in real time